PRE-FIRE INSPECTION CHECKLIST

At the time of the inspection, please be sure to have the following available for review:

- Record of annual fire alarm system tests

- Elevator inspection certificate(s)

- Record of 6 month inspection of kitchen hood AES systems

- Record of 6 month cleaning of kitchen hoods

- Record of annual fire sprinkler system inspections & tests (if applicable)

- Record of annual standpipe system inspection- hose, etc (if applicable)

- Record of annual private hydrant(s) flow test (if applicable)

- Record of testing & maintenance of emergency and standby power systems (if applicable)

- Certificates are posted that indicate that each boiler has been inspected in compliance with Section 204 of the Labor Law

- Records of inspection, testing & maintenance of electrically operated partitions maintained on premises and available for inspection. NOTE: Inspection/testing/maintenance intervals are those recommended by the manufacturer

- Record of testing & maintenance of emergency generator (if applicable)

You may also want to have your staff check on the following prior to the inspection:

- Exterior fire department Siamese connections for standpipe & sprinkler systems are not obstructed, do not leak, caps are in place and fittings are not rusted and swivel feely

- Exit doors open easily and close and latch from any position

- Interior fire & smoke doors are not chocked open, open easily and automatically close and latch from any position

- Test & repair (if needed) exit signs & emergency lighting

- No storage in any means of egress (including hallways & stairways)

- No combustible storage in mechanical, elevator control, boiler & electrical rooms

- Fire extinguishers are present as needed in common areas (at lease every 75 ft or 3000 SF) and in labs, computer rooms, mechanical/elevator control/boiler/electrical rooms & in teachers lounges (with food warming or cooking appliances)

- Fire extinguishers are mounted, not obstructed and their tags show current annual inspection date

- Extension cords not in use, other than for temporary use.

- Power strips have surge protection/circuit breaker, are not piggy backed into one another and are directly connected to receptacles (no extension cords).

- Portable electric space heaters are UL approved, have a tip over safety switch & are directly connected to a receptacle (not a power strip).

A quick survey of these issues, in addition to keeping your buildings safe, will simplify & speed the inspection process.

REMINDER: We’ll need the fire inspection labels that are attached to the annual fire inspection letter that is sent to you by the SED.